## Slide 1: Introduction to Modern Cellular Networks Part 3: 4G LTE Network Architecture and Radio Access Network (RAN) Protocols
Dejan Vukobratovic, Professor

## Slide 2: Outline of the Lecture
Overview of 3GPP LTE System Architecture
LTE Radio Access Network (RAN) Protocols

## Slide 3: 4G LTE System Architecture
Evolved Packet System (EPS)
  Generic name for 4G LTE system architecture
  Consists of two parts: RAN and EPC
Radio Access Network (RAN)
  Responsible for all radio-related functionality (scheduling, radio resource handling, retransmission protocols, coding, multi-antenna systems, etc.)
Evolved Packet Core (EPC)
  Everything else apart from radio interface (authentication, charging, end-to-end connection setup).
  Functional split: EPC may serve different radio technologies

## Slide 4
Main Architecture Blocks and Interfaces
EPC is based on packet-switched (IP) data transmission
Contains user plane and control plane interfaces and logical blocks
Several logical blocks may be part of a single physical node
Evolved Packet Core (EPC)

## Slide 5
Packet Gateway (PGW)
  Connects EPC to the Internet (central mobile network router)
  Handles allocation of IP addresses to each UE
  Implements Quality of Service (QoS) according to the defined policies
  Mobility anchor to other non-3GPP networks (e.g., CDMA 2000)
Packet Gateway (PGW)

## Slide 6
Mobility Management Entity (MME)
  Main signalling (control-plane) node of EPC
  Also called Non-Access Stratum (NAS)
  Connection and release of bearers to each user equipment (UE)
  Handling activity of connections (ACTIVE/IDLE states)
Mobility Management Entity (MME)

## Slide 7: Serving Gateway (SGW)
Serving Gateway (SGW)
  Data forwarding node between eNBs and PGW
  User-plane node connecting EPC to the RAN
  Serves as mobility anchor as mobile terminals move between eNBs and for other 3GPP technologies (GSM/HSPA)
  Collection of information and statistics needed for charging

## Slide 8: Network Elements (HSS/PCRW)
Home Subscriber Service (HSS)
  Data base containing subscriber information
Policy and Charging Rules Function (PCRF)
  Responsible for QoS handling and charging

## Slide 9: LTE System Architecture and Interfaces
Figures: These figures are taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figures 8.1 and 8.2, page 110)

## Slide 10: LTE Bearers
  IP connections (tunnels) that connect UE to packet data network (Internet)
  At least one (default) bearer is established between UE and PGW
  Bearer concatenates three tunnels: S5, S1, and Radio bearer

## Slide 11: Outline of the Lecture
Overview of 3GPP LTE System Architecture
LTE Radio Access Network (RAN) Protocols

## Slide 12: Radio Access Network and eNB node
evolved Node B (eNB) – Base station
  LTE RAN is flat in architecture – contains only base stations (eNB)
  eNB is logical node and can be implemented in various ways:
    Standard three-sector macro-cellular site
    Baseband processing unit (BBU) with a number of remote radio heads (RRH)
      Indoor base station systems with distributed antennas
      Highway base stations with many antennas along the highway
eNB Interfaces
  S1-U user data interface towards SGW/PGW
  S1-C control plane interface towards MME
  X2 interface towards neighboring eNBs
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 8.1, page 110)

## Slide 13: Radio Access Network Architecture
RAN architecture
  4 protocols (PDCP/RLC/MAC/PHY) covering L1/L2 functionality
  serve both user data (IP packets) and control data (NAS/RRC messages)
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 8.3, page 112)

## Slide 14: Radio Access Network Architecture
RAN architecture
  RAN protocols (PDCP/RLC/MAC/PHY) enable establishing radio bearer
  Other bearers (S1 and S5/S8) use GPRS tunneling protocol (GTP) to tunnel IP data to/from EPC nodes (SGW and PGW) in order to establish EPS bearer

## Slide 15: Radio Access Network Architecture
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 8.4, page 112)
Packet Data Convergence Protocol PDCP
Performs IP header compression using ROHC (Robust Header Compression)
Data ciphering
Integrity check of control data packets
In-sequence delivery and duplicate removal (during handover)
One PDCP entity per radio bearer

## Slide 16: Radio Access Network Architecture
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 8.4, page 112)
Radio Link Control Protocol RLC
Segmentation/concatenation to create variable size RLC PDUs based on scheduler decisions
RLC retransmission using ARQ mechanism
Duplicate detection and in-sequence delivery to PDCP
One RLC entity per radio bearer

## Slide 17: Radio Access Network Architecture
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 8.4, page 112)
Medium Access Control Protocol MAC
Provides services to RLC in the form of logical channels
Performs multiplexing of logical channels
Uplink and downlink scheduling (located at eNB for both UL/DL)
Hybrid ARQ (HARQ) retransmissions
MAC frame size aligned to PHY transport block (TB) size which depends on PHY configuration

## Slide 18: Radio Access Network Architecture
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 8.4, page 112)
Physical Layer Protocol PHY
Provides services to MAC layer in the form of physical channels
Error correction coding and decoding
Adaptive modulation and OFDM resource grid mapping
MIMO antenna system signal processing

## Slide 19: Radio Access Network Architecture
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 8.5, page 114)

## Slide 20: Logical, Transport and Physical Channels
Logical channels
  Interface between RLC and MAC
  Different logical channels are mapped onto transport channels
Transport channels
  Interface between MAC and PHY
  Different transport channels are mapped onto physical channels
Physical channels
  Carry transport blocks
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 8.1, page 110)

## Slide 21: Logical, Transport and Physical Channels (Downlink)
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 8.7, page 117)
Logical Channels
PCCH – Paging Control Channel
BCCH – Broadcast Control Channel
CCCH – Common Control Channel
DTCH – Dedicated Traffic Channel
DCCH – Dedicated Control Channel
MTCH – Multicast Traffic Channel
MCCH – Multicast Control Channel

## Slide 22: Logical, Transport and Physical Channels (Downlink)
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 8.7, page 117)
Transport Channels
PCH – Paging Channel
BCH – Broadcast Channel
DL-SCH – Downlink Shared Channel
MCH – Multicast Channel

## Slide 23: Logical, Transport and Physical Channels (Downlink)
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 8.7, page 117)
Physical Channels
PBCH – Physical Broadcast Channel
PDSCH – Physical Downlink Shared Channel
DCI – Downlink Control Information
PMCH – Physical Multicast Channel

## Slide 24: Logical, Transport and Physical Channels (Uplink)
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 8.8, page 118)
Logical Channels
CCCH – Common Control Channel
DTCH – Dedicated Traffic Channel
DCCH – Dedicated Control Channel
Transport Channels
UL-SCH – Uplink Shared Channel
RACH – Random Access Channel
Physical Channels
PUSCH – Physical Uplink Shared Channel
PUCCH – Physical Uplink Control Channel
PRACH – Physical Random Access Channel

## Slide 25: Takeaway Message
We reviewed 3GPP 4G LTE system architecture and explained the role of all logical blocks in the Evolved Packet Core networks
Then, we focused on Radio Access Network and investigated protocols that enable RAN communication: PDCP, RLC, MAC and PHY layer protocols. For the most of the course, PHY layer will be the focus of our exploration

## Slide 26: Further Reading
4G Book, Chapter 8

## Slide 27: Introduction to Modern Cellular Networks Part 3: 4G LTE Network Architecture and Radio Access Network (RAN) Protocols
Dejan Vukobratovic, Professor