## Slide 1: Introduction to Modern Cellular Networks Part 4: 5G NR Network Architecture and Radio Access Network (RAN) Protocols
Dejan Vukobratovic, Professor

## Slide 2: Outline of the Lecture
Overview of 3GPP NR System Architecture
NR Radio Access Network (RAN) Protocols

## Slide 3: Preliminaries
4G LTE is based on split architecture: RAN + EPC
The same principle is preserved in 5G NR: 5G Core + 5G RAN
5G RAN can be connected to 4G LTE EPC
  Non-Stand-Alone (NSA) 5G NR (first stage of 5G deployment)
  5G RAN connected to 5G Core will represent Stand-Alone (SA) deployment
  4G LTE will be also compatible with 5G Core
This is in contrast with transition from 3G to 4G where RAN/Core networks of different technologies were not compatible

## Slide 4: 5G Core Network
Three major features of 5G Core:
  Service-based architecture
    Architectures focuses on services and functionalities, not on nodes
    Due to virtualization of core network functions
  Support for network slicing
    Slice is a logical network deployed on a same physical core and RAN and providing specific services (e.g., two slices could be eMBB and URLLC)
  Control-plane/User-plane split
    Independent deployment and management of control and user plane functionality

## Slide 5: High-Level 5G Core Network Architecture
Figures: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.1, page 74)

## Slide 6: User Plane Function (UPF)
Figures: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.1, page 74)
User Plane Function
  Gateway between RAN and external networks (Internet)
  Packet routing and forwarding
  QoS handling
  Packet inspection and filtering
  Traffic measurements
  Anchor point for intra-RAT handover

## Slide 7: Session Management Function (SMF)
Figures: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.1, page 74)
Session Management Function
  Handles IP address allocation to User Equipment
  Control of policy enforcement
  General session management

## Slide 8: Access and Mobility Management Function (AMF)
Figures: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.1, page 74)
Access and Mobility Management Function
  Control Signaling between the Core and the device
  User data security
  Authentication
  Idle-state mobility
  Functionality operating between AMF and device – Non-Access Stratum (NAS)

## Slide 9: Various Network Management Functions
Figures: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.1, page 74)
Policy Control Function (PCF)
  Definition of Policy Rules
Unified Data Management (UDM)
  Authentication Credentials and access authentication
Network Exposure Function (NEF)
NR Repository Function (NRF)
Application Function (AF)

## Slide 10: 5G Core Network Function Virtualization
5G Core Network Functions can be implemented as:
  A single physical node
  A set of distributed physical nodes
  Virtualized in a centralized cloud platform
  Virtualized and distributed across edge/fog/cloud
Mobile operators are transitioning to cloud-based virtualized CN
  All CN functions are software-based and virtualized
  Flexible deployment and scaling (adding additional virtual machines)

## Slide 11: 4G and 5G Interworking
To allow early 5G deployment, NR RAN can be supported by 4G EPC
  Non-Stand-Alone deployment (Option 3)
  All control-related functions are handled by LTE, NR is used for user-data
With 5G Core deployment, NR RAN can directly connect to 5GC
  Stand-Alone operation (Option 2)
Figures: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.2, page 75)

## Slide 12: Outline of the Lecture
Overview of 3GPP NR System Architecture
NR Radio Access Network (RAN) Protocols

## Slide 13: 5G Radio Access Network Elements
5G Radio Access Network contains two types of base stations:
  gNB – serving NR devices using both NR user- and control-plane
  ng-eNB – serving LTE devices using LTE user- and control-plane
Next-Generation RAN (NG-RAN): 5G RAN consists of ng-eNB to serve LTE devices and gNB to serve NR devices
Flat architecture with ng-eNB/gNB elements

## Slide 14: 5G RAN gNB Element
gNB Element
  All radio-related functions in one or several cells
    Radio resource management, admission control, connection establishment
  Routing of user data to UPF and control information to AMF
  QoS management per packet flow
gNB is a logical node and not a physical implementation
  Standard three-sector macro-cellular site
  Baseband processing unit (BBU) with a number of remote radio heads (RRH)
  Disagregated gNB based on Open-RAN (O-RAN) specifications

## Slide 15: 5G RAN gNB Splitting
Figures: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.3, page 77)
NG Interface
  Connects gNB to 5G Core
  Separate user-plane (NG-u) and control-plane (NG-c)
  One gNB can have multiple NG interfaces for load sharing and redundancy
Xn Interface
  Similar to X2 in LTE
  Active mode mobility
  Dual-connectivity
  Joint gNB signal processing

## Slide 16: 5G RAN gNB Element
Figures: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.3, page 77)
F1 Interface
  Enables gNB Functional Split
  gNB Central Unit (gNB-CU)
  gNB Distributed Unit (gNB-DU)
  gNB-CU: Higher layer protocols (SDAP, PDCP, RRC)
  gNB-CU: Lower layer protocols (RLC, MAC, PHY)

## Slide 17: 5G gNB Dual Connectivity
Figures: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.4, page 78)
Dual Connectivity
  Allowing the device (UE) to connect to multiple cells
  Useful to increase aggregate data rate of the user
  Useful also for Non-Stand-Alone (NSA) deployment (figure)
    LTE master cell handles C-plane connection
    NR secondary cell handles U-plane connection

## Slide 18
Radio Access Network Architecture
Figures: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.6, page 80)

## Slide 19: RAN Protocols
Similar to 4G LTE
  Most notable difference is a new SDAP layer for QoS handling
  SDAP is not used in case gNB is connected to EPC
Figure: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.7, page 81)

## Slide 20
Service Data Application Protocol SDAP
New layer in 5G NR RAN
Maps QoS flows to Radio bearers according to their QoS requirements

## Slide 21: Service Data Application Protocol (SDAP)
Figures: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.5, page 79)

## Slide 22
Packet Data Convergence Protocol PDCP
Performs IP header compression using ROHC (Robust Header Compression)
Data ciphering
Integrity check of control data packets
In-sequence delivery and duplicate removal (during handover)
One PDCP entity per radio bearer

## Slide 23
Radio Link Control Protocol RLC
Segmentation to create variable size RLC PDUs based on scheduler decisions
Concatenation is removed due to delay
RLC retransmission using ARQ mechanism
Duplicate detection
Unlike LTE, NR does not support in-sequence delivery to PDCP to reduce delay
One RLC entity per radio bearer

## Slide 24: Radio Link Control Protocol (RLC)
Figures: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.10, page 85)

## Slide 25
Medium Access Control Protocol MAC
Provides services to RLC in the form of logical channels
Performs multiplexing of logical channels
Uplink and downlink scheduling (located at eNB for both UL/DL)
Hybrid ARQ (HARQ) retransmissions
MAC frame size aligned to PHY transport block (TB) size which depends on PHY configuration
Minor changes in header format in 5G NR to allow for support for low-latency processing

## Slide 26
Physical Layer Protocol PHY
Provides services to MAC layer in the form of physical channels
Error correction coding and decoding
Adaptive modulation and OFDM resource grid mapping
MIMO antenna system signal processing

## Slide 27: DL Packet Flow in 5G NR RAN Protocols
Figure: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.7, page 81)

## Slide 28: 5G NR Logical Channels
MAC layer provides service to RLC layer in the form of logical channels
Logical channels defined by the type of information they carry
  Control channels (control information) and Traffic channels (user data)
BCCH (Broadcast Control Channel)
  Delivers system information to all devices in the cell
PCCH (Paging Control Channel)
  Paging devices in the network whose location is not known
CCCH (Common Control Channel)
  Delivery of control information and for random access
DCCH (Dedicated Control Channel)
  Delivery of control information to/from a device
DTCH (Dedicated Traffic Channel)
  Delivery of user data to/from a device

## Slide 29: 5G NR Transport Format Selection
PHY layer provides service to MAC layer in the form of transport channels
How and with what characteristics are data transmitted over radio interface?
Data is organized into Transport Blocks (TB)
Transport Block is transmitted within Transmission Time Interval (TTI)
Details on how TB is transmitted are placed in Transport Format (TF) associated to each TB
TF contains information about: Transport Block Size (TBS), Modulation and Coding Scheme (MCS), Antenna Mapping
Transport Format Selection: MAC scheduler varies Transport Format in order to realize different data rates

## Slide 30: 5G NR Transport Channels
BCH (Broadcast Channel)
  Uses fixed transport format to transmit Master Information Block
PCH (Paging Channel)
  Transmission of paging information
DL-SCH (Downlink Shared Channel)
  Main transport channel used for DL data. It supports dynamic data rate adaptation, channel dependent scheduling, HARQ, spatial multiplexing, etc.
UL-SCH (Uplink Shared Channel)
  Transport channel used for UL data.
RACH (Random Access Channel)
  Dedicated for random access procedure

## Slide 31: Logical, Transport and Physical Channels
Figure: The figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “5G NR: The Next Generation Wireless Access Technology,” Academic Press (Elsevier), 2017 (Figures 6.11, page 88)

## Slide 32: Takeaway Message
We reviewed 3GPP 5G LTE system architecture and explained the role of all logical blocks in 5G Core Network and differences with 4G LTE EPC
Then, we focused on Radio Access Network and investigated protocols that enable RAN connection and pointed out to the minor differences compared to 4G LTE RAN

## Slide 33: Further Reading
5G Book, Chapter 6

## Slide 34: Introduction to Modern Cellular Networks Part 4: 5G NR Network Architecture and Radio Access Network (RAN) Protocols
Dejan Vukobratovic, Professor