## Slide 1: Introduction to Modern Cellular Networks Part 5: 4G LTE Radio Interface – Part 1
Dejan Vukobratovic, Professor

## Slide 2
4G LTE Radio Interface
4G LTE radio interface is designed to deliver IP packets from the base station (eNB) to the mobile device (UE) in the downlink, or vice versa in the uplink
After processing IP packets on layer 2 via PDCP, RLC and MAC sublayers (see part 3 and 4 lectures), MAC frames are delivered to physical layer (PHY) for physical signal transmission
LTE PHY is the key part and it is worth introducing its basics!

## Slide 3
4G LTE PHY Signal Processing

## Slide 4
4G LTE PHY Signal Processing
MAC
PHY
CRC, FEC CODING, RATE MATCHING, SCRAMBLING
0
1
0
0
0
1
1
0
1
0
1
1
0
MODULATION, RESOURCE GRID MAPPING
0
1
0
0
0
1
1
0
1
0
1
1
0
0
1
0
1
1
0
K bits
N bits
Turbo Codes
QPSK, 16-QAM, 64-QAM
PHY signals
PHY channels
OFDM MODULATION
RF

## Slide 5
4G LTE PHY Signal Processing
MAC
PHY
CRC, FEC CODING, RATE MATCHING, SCRAMBLING
0
1
0
0
0
1
1
0
1
0
1
1
0
MODULATION, RESOURCE GRID MAPPING
0
1
0
0
0
1
1
0
1
0
1
1
0
0
1
0
1
1
0
K bits
N bits
Turbo Codes
QPSK, 16-QAM, 64-QAM
PHY signals
PHY channels
OFDM MODULATION
RF

## Slide 6: Outline of the Lecture
Basics on Error Correction Codes
Error Correction Coding in 4G LTE
Modulation Schemes in 4G LTE

## Slide 7: Error Correction Mechanisms
Two main approaches to error correction
Forward Error Correction (FEC)
  Use FEC encoding at the Tx side and FEC decoding at Rx side to achieve reliable information transmission across noisy channels
  Implemented across message bits at the PHY layer (L1)
Automatic Repeat Request (ARQ)
  Use feedback messages (ACK/NACK) to request packet retransmission
  Implemented at the DLL layer (L2) – in 4G LTE that is RLC layer
  Possible combination of FEC and ARQ is called Hybrid-ARQ

## Slide 8: Forward Error Correction Solution
Use communication channel as it is!
Improve system design by including FEC encoder at the transmitter and FEC decoder at the receiver side
  Digital FEC processing results in low-cost chip design and implementation
Figure: This figure is taken from D. MacKay: “Information Theory, Inference and Learning Algorithms,” Cambridge University Press, 2003 (Figure 1.6, page 5)

## Slide 9: Forward Error Correction Solution
Basic Idea: Encode the binary information message by introducing (in a smart way) additional (redundant, protection) bits that will be used at the receiver to recover from channel-induced errors
Cost:
  Message encoding at the transmitter
  Message decoding at the receiver
  Transmission of redundant bits
Benefit:
  Reduction in bit error rates compared to uncoded data transmission over a given channel

## Slide 10: Forward Error Correction Solution
Source message of length K bits
Encoder maps the source message 1-on-1 to a corresponding codeword of length N bits
  In other words, adds N-K redundant bits
Codeword is transmitted over a noisy channel
  Channel is defined using a channel model
Received sequence generally differs from a transmitted codeword
Taking received sequence as an input, Decoder provides an estimate of the transmitted codeword/source message

## Slide 11: Code Rate
Code Rate is the main parameter of FEC encoded system
  R = K/N
Describes number of information (useful) bits transmitted per each bit transmitted through the channel
  0 ≤ R ≤ 1 (for binary input channels)
Target: Design FEC encoded system in which the probability of bit error tends to zero with as large as possible code rate R
  The larger R, the less redundant bits are added

## Slide 12: Channel Capacity
Question: With how high R we can go while keeping bit error probability Pe close to zero (reliable transmission)?

## Slide 13: Outline of the Lecture
Basics on Error Correction Codes
Error Correction Coding in 4G LTE
Modulation Schemes in 4G LTE

## Slide 14: Error Correction Coding in 4G LTE
CHANNEL
Encoder/Decoder

## Slide 15: Error Correction Coding in 4G LTE
FEC coding is part of DL-SCH transport channel processing
Input from MAC layer – Transport Block (TB)
Step 1 – CRC Encoding
  Attach 24-bit CRC-24 error detection code to TB
  Allows for error detection at the receiver
  Used to trigger HARQ retransmissions

## Slide 16: Error Correction Coding in 4G LTE
Step 2 – Code Block Segmentation
  LTE Turbo Code has a limitation on the length of the input information sequence equal 6144 bits
  If TB + CRC-24 exceeds this size: Code block segmentation
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 10.2, page 145)

## Slide 17: Error Correction Coding in 4G LTE
Step 3 – Turbo Coding
  LTE uses R=1/3 Turbo Code, with input blocks from 40:6144 bits
  Redundancy Version (RV) selection for HARQ is using circular buffer
  Rate-matching matches No of bits to be transmitted to available resources
Step 4 – Scrambling
  Randomizes interference from neighboring cells
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 10.5, page 147)

## Slide 18: DL-SCH Transport Block Processing
Figure: This figure is taken from E. Dahlman, S. Parkvall, J. Skoll: “4G LTE/LTE-Advanced for Mobile Broadband,” Academic Press (Elsevier), 2011 (Figure 10.1, page 144)
Binary Sequence Processing
Complex Sequence Processing

## Slide 19
4G LTE PHY Signal Processing
MAC
PHY
CRC, FEC CODING, RATE MATCHING, SCRAMBLING
0
1
0
0
0
1
1
0
1
0
1
1
0
MODULATION, RESOURCE GRID MAPPING
0
1
0
0
0
1
1
0
1
0
1
1
0
0
1
0
1
1
0
K bits
N bits
Turbo Codes
QPSK, 16-QAM, 64-QAM
PHY signals
PHY channels
OFDM MODULATION
RF

## Slide 20: Outline of the Lecture
Basics on Error Correction Codes
Error Correction Coding in 4G LTE
Modulation Schemes in 4G LTE

## Slide 21: Modulation Schemes in 4G LTE
Modulation schemes used in LTE include:
  QPSK (Quadrature Phase Shift Keying)
  16-QAM (Quadrature Amplitude Modulation)
  64-QAM (Quadrature Amplitude Modulation)

## Slide 22: QPSK Modulation in 4G LTE
QPSK maps two input bits to one of four modulation symbols
Mapping scheme is presented in the table below
Figure: This table is taken from Zarrinkoub, H., “Understanding LTE with MATLAB: from mathematical modeling to simulation and prototyping,” John Wiley & Sons (Table 4.1, page 73)

## Slide 23: 16-QAM Modulation in 4G LTE
16-QAM maps four input bits to one of 16 modulation symbols
Mapping scheme is presented in the table to the right
Figure: This table is taken from Zarrinkoub, H., “Understanding LTE with MATLAB: from mathematical modeling to simulation and prototyping,” John Wiley & Sons (Table 4.2, page 73)

## Slide 24: 64-QAM Modulation in 4G LTE
64-QAM maps six input bits to one of 64 modulation symbols
Multiple available modulation schemes are instrumental for Adaptive Coding and Modulation
Based on received Signal-to-Noise Ratio (SNR) the device switches between modulation schemes

## Slide 25: Takeaway Message
We reviewed basics of Forward Error Correction coding and its connection to Channel Capacity in Information Theory
We explained how Turbo Codes are applied in LTE physical layer, along with CRC detection, code block segmentation and scrambling
We presented basic Modulation schemes used in 4G LTE and presented their constellation diagrams

## Slide 26: Introduction to Modern Cellular Networks Part 5: 4G LTE Radio Interface – Part 1
Dejan Vukobratovic, Professor