## Slide 1: Introduction to Modern Cellular Networks Part 7: Introduction to Cellular IoT
Dejan Vukobratovic, Professor

## Slide 2: Outline of the Lecture
Introduction to Internet of Things
Introduction to IoT in Mobile Cellular Networks
Competing Technologies in Unlicenced Spectrum
Example Applications of Cellular IoT

## Slide 3: Introduction to Internet of Things
The concept of extending the Internet to connect everything
Traditional cellular subscriptions are saturated (~ 7 billion)
What is new that is going to be connected?
  Sensors, meters, home appliances, infrastructures (gas, water, electricity), bicycles, cars, drones, wearable devices, and many more
Already between 20-25 billion connected devices in 2020.

## Slide 4: Short-Range Internet of Things – The First Wave
IoT concept is around for at least a decade
  Wireless Sensor Networks
  Smart Homes, Smart Wearables
Relies on Short-Range IoT
  Bluetooth Low Energy (BLE)
  Near-Field Communications (NFC)
  IEEE 802.15.4 based ZigBee devices
  IEEE 802.11 based Wi-Fi devices
Limited to 10-100 meters range
Rico-Alvarino, et al., “An overview of 3GPP enhancements on machine to machine communications,” IEEE Communications Magazine, 54(6), pp.14-21, 2016.

## Slide 5
https://www.ericsson.com/en/mobility-report/reports/november-2017/internet-of-things-outlook
Evolution of Internet of Things
Wide-area IoT grows at fastest pace (30% per year)

## Slide 6: Long-Range Internet of Things – The Second Wave
LP WAN: Extension of IoT concepts to large coverage areas
  Low-Power Wide Area Networks
Long-Range IoT
  Cellular Networks
  Unlicenced-band solutions
    LoRa, SigFox
  Licenced-band solutions
    Cellular IoT Standards
    Machine-Type Communications
Rico-Alvarino, et al., “An overview of 3GPP enhancements on machine to machine communications,” IEEE Communications Magazine, 54(6), pp.14-21, 2016.

## Slide 7: Outline of the Lecture
Introduction to Internet of Things
Introduction to IoT in Mobile Cellular Networks
Competing Technologies in Unlicenced Spectrum
Example Applications of Cellular IoT

## Slide 8: Internet of Things in Mobile Cellular Networks
Traditional cellular networks support:
  standard-compliant mobile handsets (UE)
  GPRS/3G/4G modems
  3G/4G USB dongles
Not suitable for IoT vision, as these devices are:
  Not low-power and low data-rate
  Not supported in massive connectivity scenario
In recent years 3GPP invested significant effort to offer new mobile cellular IoT standards

## Slide 9: Requirements for Machine-Type Communications
Dawy, Z., Saad, W., Ghosh, A., Andrews, J.G. and Yaacoub, E., 2017.
Toward massive machine type cellular communications. IEEE Wireless Communications, 24(1), pp. 120-128.

## Slide 10: Development of Machine-Type Communications
Work on MTC in cellular networks initiated in 3GPP in 2011 (Rel. 12)
  Study item: Study on Provision of Low-Cost MTC UEs Based on LTE
  Replace GPRS/EGPRS as a default bearer for MTC services
  Bring device complexity and cost to GPRS/EGPRS device levels
This work is extended and first standards completed in 2016 (Rel. 13)
  Study item: Cellular System Support for Ultra-low Complexity and Low Throughput Internet of Things
  Goals shifted from replacing GPRS/EGPRS to provide competing LP WAN solution
  Ultra-low device complexity, extreme coverage range and long device battery life

## Slide 11: Main Requirements
Extended Coverage
  20dB extension over 4G LTE
Extended Battery Lifetime
  Utility meters w/o access to power supply
  Reduce long-term operational costs
Network capacity
  Central London use case
  40 devices per household
  60.000 devices per km2
As low as possible device cost
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Table 1.1, page 8.

## Slide 12: Machine-Type Communications (MTC) Standards
enhanced Machine-Type Communications (eMTC/LTE-M)
  Cat-0 (6 PRB – 1.08 MHz)
Narrow-Band Internet of Things (NB-IoT)
  Low-power Low-cost (1 RB – 180 kHz)
Extended Coverage GSM IoT (EC-GSM-IoT)
  Cat-0 (6 PRB – 1.08 MHz)
3GPP Release 13 (2016)
Rico-Alvarino, et al., “An overview of 3GPP enhancements on machine to machine communications,” IEEE Communications Magazine, 54(6), pp.14-21, 2016.
Shariatmadari, et al. “Machine-type communications: current status and future perspectives toward 5G systems,” IEEE Communications Magazine, 53(9), pp. 10-17, 2015.

## Slide 13: Cellular IoT in 5G: mMTC and URLLC

## Slide 14: Cellular IoT in 5G: Service Requirements
massive Machine-Type Communications (mMTC)
  106 devices/km2 satisfying packet loss rates less than 1%.
Ultra-Reliable Low-Latency Communications (URLLC)
  Generic DL/UL latency target is 0.5 ms
  Reliability targets packet loss rate of 10-5 for 32 byte packets and 1ms latency
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 1.1, page 5.

## Slide 15: Outline of the Lecture
Introduction to Internet of Things
Introduction to IoT in Mobile Cellular Networks
Competing Technologies in Unlicenced Spectrum
Example Applications of Cellular IoT

## Slide 16: Competing LP WAN Technologies
ISM bands (USA)
Unlicenced Spectrum IoT
  Use available ISM bands
    Public, free-to-use
    Regulated transmission limits
  Best known IoT standards
    Short-to-medium range
    Bluetooth Low Energy, ZigBee
    IEEE 802.11ah HaLow (Wi-Fi IoT)
  First commercial LP WAN standards
    LoRaWAN
    SigFox

## Slide 17: LP WAN Technologies: SigFox
French start-up established in 2009 based in Toulouse
SigFox exploits very low bandwidth to reduce SNR
Ultra narrowband modulation; MPL of 162 dB
12B messages up to 140 times per day using 100 bps data rate
ISM bands: 868 MHz in Europe and 902 MHz in USA
Many networks in Europe including national-wide coverage in France, Spain and Portugal
http://www.sigfox.com

## Slide 18: SigFox Limitations
The number of messages is limited to 140/day – Why?
  This is due to EU regulation for unlicenced spectrum
  Device may use public band up to 1% of the total time
  With 100 bps data rate, this translates to 6 messages of 12 bytes per hour or equivalently 140 messages per day
  Downlink messages are up to 8 bytes in size
  Base station can send at least 4 messages per day to each device
http://www.sigfox.com - Sigfox Technical Overview Whitepaper

## Slide 19: SigFox Network Architecture
http://www.sigfox.com - Sigfox Technical Overview Whitepaper

## Slide 20: SigFox Network Architecture
http://www.sigfox.com - Sigfox Technical Overview Whitepaper
Network Equipment layer
  Contains SigFox base stations
  Delivers messages between devices and support system
Support System layer
  SigFox Core Network
  Processes device messages
  Entry point to different SigFox actors via web interfaces or various APIs
Connection between the layers is via Internet through secure VPN tunnels

## Slide 21: LP WAN Technologies: LoRaWAN
Originally developed by Cyclos in France, acquired by Semtech
Now supported by LoRa Alliance, consortium of 500+ members
LoRa exploits Chirp Spread Spectrum modulation to reduce SNR
MCL of 154 dB in 868 MHz band in EU and 902 MHz in USA
LoRa defines PHY layer, LoRaWAN defines MAC layer
http://www.lora-alliance.org

## Slide 22: LoRa Physical Layer
LoRa Physical Layer optimized for low-power and extremely long range communications
  FSK is traditionally used for long-range
  LoRa uses Chirp Spread Spectrum
    Similar power costs but extended range compared to FSK
Chirp Spread Spectrum
  Used in military and space communications for decades
  LoRa is the first commercial system that uses CSS
http://www.lora-alliance.org

## Slide 23: Chirp Spread Spectrum
Chirp pulse is combined with On-Off Keying (OKK)
  Simple binary modulation using Up-Chirp and Null-Chirp
  More complex modulations can be designed using both Up-Chirp and Down-Chirp in combination with Null-Chirp
  Data payload ranges between 2-255 bytes
Spectrum Allocation
  LoRa uses different Sub-GHz ISM bands
t
f
1 0 1 0 0 1
flow
fhigh
Chirp pulse
OOK with Null and Up-Chirp
http://www.lora-alliance.org – A Technical Overview of LoRa and LoRaWAN

## Slide 24
LoRaWAN Network Architecture
http://www.lora-alliance.org – A Technical Overview of LoRa and LoRaWAN

## Slide 25: LoRa MAC Layer: LoRaWAN
LoRaWAN Random Access
  LoRa devices do not associate to specific Gateway
  Data is recovered by possibly multiple Gateways
  Packet duplicates are filtered by the Network Server
LoRaWAN Gateway
  Listens for device packets
    Uses one of possible 9 channels in 868 MHz band in Europe
  Any recovered packet is forwarded to the Network Server
LoRa Network Server
  Network management, filtering redundant packets, acknowledgements, security checks, etc.
http://www.lora-alliance.org

## Slide 26: Outline of the Lecture
Introduction to Internet of Things
Introduction to IoT in Mobile Cellular Networks
Competing Technologies in Unlicenced Spectrum
Example Applications of Cellular IoT

## Slide 27: CIoT Application Examples
Figure: https://iot.t-mobile.com/narrowband/

## Slide 28: CIoT Smart Metering
Figure: https://www.kamstrup.com/en-en/products-solutions/meter-reading/sigfox-and-nb-iot
Figure: https://www.fiorentini.com/ww/en/pietro_fiorentini _pioneer_in_the_development_of_nbiot_technology

## Slide 29: CIoT Pet Collars
Figure: https://getrawr.com/

## Slide 30: CIoT Smart Parking Applications
Figure: https://iot.telekom.com/en/products/park-joy/

## Slide 31: CIoT GPS Tracker (Logistics/Fleet Management)
Figure: https://www.mictrack.com/product/nb-iot-gps-tracker/

## Slide 32: CIoT Luggage Trackers
Figure: https://accent-systems.com/project/trackgo-locate-your-lost-luggage/

## Slide 33: CIoT Connected Cows
Figure: https://www.huawei.com/minisite/iot/en/connected-cows.html

## Slide 34: Introduction to Modern Cellular Networks Part 7: Introduction to Cellular IoT
Dejan Vukobratovic, Professor