## Slide 1: Introduction to Modern Cellular Networks Part 8: Introduction to NB-IoT
Dejan Vukobratovic, Professor

## Slide 2: Outline of the Lecture
Introduction to NB-IoT (Architecture, Resource Grid)
Detailed Pass Through a Single NB-IoT Uplink Packet Transmission

## Slide 3
Preliminaries: NB-IoT System Architecture
SGW
IoT
Platform
CIoT UE
MME
PGW
SCEF
C-SGN
E-UTRAN
CIoT EPC
Application
Servers
eNB
CIoT UE
CIoT UE
eNB – BASE STATION
MME – MOBILITY MANAGEMENT ENTITY
SCEF – SERVICE CAPABILITY EXPOSURE FUNCTION
C-SGN – CIoT – SERVING GATEWAY NODE
SGW – SERVING GATEWAY
PGW – PACKET GATEWAY

## Slide 4
Preliminaries: NB-IoT RAN Protocols
MQTT-SN
DTLS
UDP
IP
NAS
RRC
PDCP
RLC
MAC
PHY
RRC
PDCP
RLC
MAC
PHY
UDP
IP
L2
L1
NAS
UDP
IP
L2
L1
L2
L1
L2
L1
L2
L1
MQTT-SN
DTLS
UDP
IP
MQTT
DTLS
UDP
IP
eNB
MME/PGW
IoT Platform
Cloud App
APP
APP
L2
L1
MQTT
DTLS
UDP
IP
CIoT UE

## Slide 5
Preliminaries: NB-IoT PHY Signal Processing
MAC
PHY
CRC, FEC CODING, RATE MATCHING, SCRAMBLING
0
1
0
0
0
1
1
0
1
0
1
1
0
MODULATION, RESOURCE GRID MAPPING
0
1
0
0
0
1
1
0
1
0
1
1
0
0
1
0
1
1
0
K bits
N bits
Turbo Codes (UL) TBCC (DL)
BPSK and QPSK
PHY signals
PHY channels
OFDM MODULATION
RF

## Slide 6
Preliminaries: NB-IoT in Time Domain
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.4 and Figure 7.9.

## Slide 7
Preliminaries: NB-IoT in Frequency Domain
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.5, page 228.

## Slide 8
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.11, page 234.
Preliminaries: NB-IoT DL Frame Structure
  Signals:
  NPSS – Narrowband Primary Synchronization Signal
  NSSS – Narrowband Secondary Synchronization Signal
  NRS – Narrowband Reference Signal
  Channels:
  NPBCH – Narrowband Physical Broadcast Channel
  NPDCCH – Narrowband Physical Downlink Control Channel
  NPDSCH – Narrowband Physical Downlink Shared Channel

## Slide 9
Kanj, M., Savaoux, V., Le Guen, M., A Tutorial on NB-IoT Physical Layer Design, IEEE Communication Surveys and Tutorials, September 2020, Figure 7.
Preliminaries: NB-IoT DL Frame Structure

## Slide 10
Preliminaries: NB-IoT UL Frame Structure
  Signals:
  DMRS – Demodulation Reference Signal
  Channels:
  NPRACH – Narrowband Physical Random Access Channel
  NPUSCH – Narrowband Physical Uplink Shared Channel
Andres-Maldonado, P., Ameigeiras, P., Prados-Garzon, J., Navarro-Ortiz, J., & Lopez-Soler, J. M. (2017). Narrowband IoT data transmission procedures for massive machine-type communications. IEEE Network, 31(6), 8-15.

## Slide 11: Outline of the Lecture
Introduction to NB-IoT (Architecture, Resource Grid)
Detailed Pass Through a Single NB-IoT Uplink Packet Transmission

## Slide 12
NB-IoT Uplink Data Transmission Phases
Downlink transmission
Uplink transmission

## Slide 13
Cell Search and Synchronization
Downlink transmission
Step 1: Search for NPSS to identify presence of an NB-IoT cell
NB-IoT uses Frame 5 (NPSS) and Frame 9 (NSSS) for synchronization
NPSS signal
Repeats every 10 ms
Used for time-frequency synch to an NB-IoT cell
After long PSM period, UE looses T/F reference
Frequency reference may be off for 20 ppm (i.e., 18 kHz @ 900 MHz carrier)
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.13, page 235.

## Slide 14
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.14, page 237.
NPSS signal structure
Base sequence p:
  Length-11 Zadoff-Chu Sequence in freq. domain
Cover sequence c = (1,1,1,1,-1,-1,1,1,1,-1,1)
Each of 11 OFDM symbols in NPSS carries a base sequence +p or -p depending on c
NB-IoT device correlates the received sequence with NPSS to detect this repetitive pattern
Narrowband Primary Synchronization Signal

## Slide 15
Narrowband Secondary Synchronization Signal
Downlink transmission
  Step 3: From NSSS, identify PCID and three LSBs of the System Frame Number (SFN)
NSSS signal
After NPSS acquires T/F synch NSSS acquires cell PCID
Physical Cell Identity – PCID: 504 possible values
NSSS cycle
Repeats every 80 ms
Four consecutive different sequences every 20 ms
Encode PCID value
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.13, page 235.

## Slide 16
NPSS/NSSS Detection in MATLAB
https://ww2.mathworks.cn/help//lte/ug/nb-iot-downlink-waveform-generation.html

## Slide 17
NB-IoT Uplink Data Transmission Phases
Downlink transmission
Uplink transmission

## Slide 18
Narrowband Physical Broadcast Channel (NPBCH)
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.17, page 241.
  Step 4: Acquire the MIB to identify complete SFN, as well as two LSBs of Hyperframe SFN (H-SFN)
NPBCH delivers Master Information Block (MIB)
MIB Cycle: 640 ms Transmission Time Interval (TTI) in sub-frame 0 of every frame
100 REs per NPBCH sub-frame
  QPSK modulated = 200 bits
TBS of NPBCH = 34 bits + CRC-16 = 50 bits
Encoded using TBCC and rate matched into a codeword of length 1600 bits
Transmitted as 8 code subblocks (CSB) of 200 bits

## Slide 19
MIB contains following data
  Operation mode (in-band, stand-alone, guard-band)
  For in-band and guard-band: frequency raster offset (+/- 2.5, 7.5 kHz)
  Four MSBs of the SFN
  Two LSBs of the H-SFN
  Information about SIB1-NB scheduling
  SI value tag
  AB (Access Barring) information
Master Information Block Acquisition

## Slide 20
NB-IoT Uplink Data Transmission Phases
Downlink transmission
Uplink transmission

## Slide 21
Random Access Preamble
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.24, page 250.
Consists of CP + 5 single-tone symbols – sinusoids at n*3.75 kHz
  Two formats of CP lengths for different cell radius
NPRACH repetition consists of 4 symbol groups with frequency hopping
  Deterministic FH pattern (tables)
  Hopping is done within groups of 12 consecutive sub-carriers
Single NPRACH repetition is usually not enough
  Up to 128 NPRACH repetitions to ensure coverage extension

## Slide 22
If eNB detects NPRACH preamble, it sends back RAR – Random Access Response RRC message – Message 2
  Contains scheduling info for sending connection request – Message 3
In Message 3, device includes its identity and scheduling request
In Message 4, eNB resolves possible contention due to preamble collisions and transmits Connection Setup/Resume RRC message
The device replies with RRC Connection Setup/Resume Complete message – Message 5, and transits to Connected Mode
Random Access Procedure

## Slide 23
Random Access Procedure
Downlink transmission
Uplink transmission
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.41, page 277.

## Slide 24
NB-IoT Uplink Data Transmission Phases
Downlink transmission
Uplink transmission

## Slide 25: Uplink Data Transmission Phase
This phase consists of a sequence of scheduling info delivered from eNB to UE via NPDCCH intergchangably with the sequence of uplink data packets delivered from UE to eNB via NPUSCH
Scheduling info is transmitted via NPDCCH channel (control channel) in the form of Downlink Control Information (DCI)
After reading DCI, device knows in which uplink subframes to send data or in which downlink subframes to expect data

## Slide 26: Narrowband Physical Downlink Control Channel (NPDCCH)
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.19, page 243.
Carries Downlink Control Information (DCI)
  UL Grant Information (DCI Format N0, 23 bits)
  DL Scheduling Information (DCI Format N1, 23 bits)
  Paging indicator or SI update (DCI Format N2, 15 bits)

## Slide 27: Narrowband Physical Uplink Shared Channel (NPUSCH)
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.9, page 255.
NPUSCH defines different RU configurations
  Occupy different “rectangular shapes” in time-frequency resource grid

## Slide 28: Narrowband Physical Uplink Shared Channel (NPUSCH)
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.28, page 258.
24-bit CRC is attached to TB, encoded using turbo code, rate matched and BPSK/QPSK modulated and mapped to appropriate set of RUs
Scrambling is applied between coding and modulation
Maximum 128 TB repetitions is possible
  Figure: TBS = (12 subcarriers, 2 RUs), 8 repetitions, scrambling reinitialized every 4 repetitions

## Slide 29: Narrowband Physical Downlink Shared Channel (NPDSCH)
NPDSCH transmits unicast data in the form of TBs
Besides data TBs, NPDCSH is used to deliver SI (e.g., SIB1-NB)
TB is appended with 24-bit CRC and TBCC coded up to 680 bits
Codewords are QPSK modulated and mapped to up to 10 SFs
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Table 7.5, page 246.

## Slide 30: Narrowband Physical Downlink Shared Channel (NPDSCH)
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.21, page 247.
Before QPSK mapping, TB bits are scrambled
Scrambling is reinitialized every min(4, NREP) repetitions (see figure)
Early decoding can be performed (e.g., in figure, after 8 SFs)
Up to 2048 repetitions (20480 frames), transmission gaps can be configured
  Figure: Two-subframe TB repeated 8 times with scrambling reinitialized every 4 repetitions

## Slide 31
NB-IoT Uplink Data Transmission Phases
Downlink transmission
Uplink transmission

## Slide 32
In Idle Mode, device periodically checks Paging messages
  Inform the device on incoming DL data
  Less frequent paging is more energy efficient, but introduces DL delays
Paging configurations in NB-IoT differ in DRX or eDRX mode
Paging and eDRX Mode
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.40, page 276.

## Slide 33
NB-IoT Uplink Data Transmission Phases
Downlink transmission
Uplink transmission

## Slide 34
Some applications have loose requirements on device reachability
PSM is most efficient sleep mode
  Device runs only real-time clock
  Does not monitor paging during PSM
  Does not maintain synchronization with the network
  Duration of PSM is configurable and can extend to extreme values
Power Saving Mode (PSM)
Liberg, O., Sundberg, M., Wang, E., Bergman, J. and Sachs, J., Cellular Internet of things: technologies, standards, and performance. Academic Press, 2017, Figure 7.21, page 247.

## Slide 35: Introduction to Modern Cellular Networks Part 8: Introduction to NB-IoT
Dejan Vukobratovic, Professor